## Slide 1: Reconciling SCXML Statechart Representations and Event-B Lower Level Semantics
Karla Morris : Sandia National Laboratories, CA, USA
Colin Snook : University of Southampton, UK

## Slide 2: Outline
Motivation
Model Representations
  SCXML
  iUML-B
  Similarities & Differences in the Semantics
Extensions to SCXML
Prototype System Model
Future Work
Conclusions

## Slide 3: Motivation
Event-B provides verification by formal proof…
… but notation is restricted to simplify verification.
Engineers are used to a richer notation..
.. they may find the restrictions difficult to accept.
iUML-B State-machines help but still close to Event-B.
Can Harel style state-chart semantics be reconciled with iUML-B?
We investigate a translation from SCXML state-charts to iUML-B state-machines (and hence to Event-B).

## Slide 4: SCXML: State Chart eXtensible Markup Language
State Chart XML :
  State Machine Notation for Control Abstraction
XML notation
Harel Statecharts
Related to CCXML Call Control XML, event-based telephony
Executable (via simulator tools)

## Slide 5: SCXML
<?xml version="1.0"?>
<scxml xmlns="http://www.w3.org/2005/07/scxml"
version="1.0"
datamodel="ecmascript"
initial="off">
<!--trivial 5 second microwave oven example -->
<datamodel>
<data id="cook_time" expr="5"/>
<data id="door_closed" expr="true"/>
<data id="timer" expr="0"/>
</datamodel>
<state id="off">
<!-- off state -->
<transition event="turn.on" target="on"/>
</state>
<state id="on">
<initial>
<transition target="idle"/>
</initial>
<!-- on/pause state -->
<transition event="turn.off" target="off"/>
<transition cond="timer = cook_time" target="off"/>
<state id="idle">
<!-- default immediate transition if door is shut -->
<transition cond="door_closed" target="cooking"/>
<transition event="door.close" target="cooking">
<assign location="door_closed" expr="true"/>
<!-- start cooking -->
</transition>
</state>
<state id="cooking">
<transition event="door.open" target="idle">
<assign location="door_closed" expr="false"/>
</transition>
<!-- a 'time' event is seen once a second -->
<transition event="time">
<assign location="timer" expr="timer + 1"/>
</transition>
</state>
</state>
</scxml>

## Slide 6: iUML-B Statemachines

## Slide 7: iUML-B Statemachines

## Slide 8: Similarities between SCXML and iUML-B
Hierarchical nested state-charts
Transitions with
  Conditions / Guards
  Actions
States can have Entry and Exit Actions
  (use with care in iUML-B)

## Slide 9: Differences between SCXML and iUML-B
iUML-B has..
  Refinement
  Invariants
  Atomic Actions
SCXML has..
  External Trigger events
    Hence transitions do not have a name/label
  Sequential actions
  Run to Completion – Big step/little step

## Slide 10: SCXML Extensions
XML tools allow new meta-model ‘namespaces’ to be introduced.
  Existing SCXML tools will ignore them
Needed in order to support:
  Refinement levels (new attribute <iumlb:refinement …>)
  Invariants (new element <iumlb:invariant …>)
  Guards (new element <iumlb:guard …>)

## Slide 11: SCXML Extension Attributes

## Slide 12: Example extended SCXML (extensions are captured in red)
<datamodel iumlb:refinement="2">
<data expr="false" id="Gate_In.Block" iumlb:type="BOOL"/>
</datamodel>
<!-- Other model details -->
<state id="BLOCKED">
<transition cond="[On_In.CardAccept==true]" target="UNBLOCKED">
<iumlb:guard name="gd1" predicate="On_In.CardAccept==true" refinement="2"/>
<assign expr="true" location="Gate_In.Block" iumlb:refinement="3"/>
</transition>
<onentry>
<assign expr="true" location="Gate_In.Block"/>
<assign expr="false" location="On_In.Reset"/>
</onentry>
<onexit>
<assign expr="false" location="Gate_In.Block"/>
</onexit>
<iumlb:invariant predicate="Gate_In.Block == TRUE" name="GateCondition"/>
</state>

## Slide 13: Initial translation supports..
Data models
Hierarchical nested statemachines
Parallel Statemachines
‘When’ Transitions (label)
Transition parameters, guards and actions
Invariants
Initial and Final states
Refinement (superposition only)

## Slide 14: Diagram of SCXML

## Slide 15: Example – generated iUML-B

## Slide 16: Next steps
Try modelling the run to completion semantics
E.g. trigger events create a token,
  A new token can only be consumed when no transitions are enabled
Try enforcing transition run-to-completion sequences
Still omit sequencing of actions

## Slide 17: First Strategy:
iUML-B Statemachines will own a collection of triggers.
  Each trigger will generate an Event-B BOOL variable.
    (Note simplification of SCXML, which permits several triggers of a kind to be queued)
  Transitions may reference a trigger.
    The reference will generate a guard, <trigger variable> = TRUE
    And an action <trigger variable> := FALSE.
  Transitions may own a collection of ‘Raise’ actions that reference an internal trigger.
    This will generate an action <trigger variable> := TRUE.
  Trigger may be designated as external event.
    An trigger event will be generated to create a new trigger (<trigger variable> := TRUE )
    when it has been consumed ( <trigger variable> = FALSE ) and
    no transitions are enabled. (run to completion)
A partial ‘run-to-completion’ semantics will be introduced by disabling all trigger events while any external or internal transition is enabled.

## Slide 18: First Strategy: External trigger event
Old trigger has been consumed
Raise new trigger
No transitions enabled

## Slide 19: First Strategy: Triggered transition
The trigger guard
Raise an internal trigger
Consume the external trigger

## Slide 20: Second Strategy:
A
B
/ raised
C
D
External Triggers
: External Triggers
Internal Trigger
AB: Trigger Transitions
BC: Trigger Transitions
BD: Trigger Transitions
Set NEXT
{ }
Set NOW
{ }
Trigger Events
Raised Trigger
No enable transitions
Step
Triggered Transitions
[trigger NOW]
a
a
b
b

## Slide 21: Second Strategy: basis
We start with a ‘basis’ Event-B machine
  Abstract representation of the run to completion ‘step’ behaviour
In Refinements
  We will add new transitions and triggers
  This will generate new events that modify old variables (NOW and NEXT)
We provide ‘basis’ events for future events to refine
  Future transitions event (parameters T, R)
    Refinements add guard to define T = {<theNewTriggers>}
    Refinements add guard to define R = {<theNewRaisedTriggers>}
  Future trigger event (parameters t)
    Refinements add guard to define t = <theNewTrigger>

## Slide 22: Second Strategy: basis

## Slide 23: Second Strategy: External trigger event
(action from basis)
Add new trigger to the NEXT set
Define new Trigger

## Slide 24: Second Strategy: Triggered transition
The trigger guard
Raise an internal trigger
(actions from basis)
Consume the external trigger and raise internal ones

## Slide 25: Second Strategy: Step Event
(actions from basis)
No transitions enabled
Problem:
if guard of an existing transition is strengthened,
corresponding guard in step is weakened

## Slide 26: Conclusions
Strong motivation from engineers
Difficult to reconcile semantic differences
  Run-to-completion, Sequential execution
We adopt a compromise
  Support what we can
    Add extensions where necessary
  Otherwise, restrict SCXML

## Slide 27: Thank you
Questions?

## Slide 28: Second Strategy:
Two phases:
  Triggers are accumulated in one phase and consumed in the next phase
  Phases overlap, next triggers are accumulated while last is consumed
Trigger events are accumulated in a set NEXT
Trigger events are consumed from a set NOW
A step event copies NEXT to NOW and clears NEXT
Raising trigger events
  An event representing an external trigger
  Or a transition with a “Raise’’ action
  All triggers are added to NEXT
A partial ‘run-to-completion’ semantics will be introduced
  by disabling the step event while any transition is enabled

## Slide 29: Next steps
Try modelling the run to completion semantics
E.g. trigger events create a token,
  A new token can only be consumed when no transitions are enabled
Try enforcing transition run-to-completion sequences
Still omit sequencing of actions

## Slide 30: Enhance iUML-B to support triggers
iUML-B Statemachines will own a collection of triggers.
  Each trigger will generate an Event-B BOOL variable.
    (Note simplification of SCXML, which permits several triggers of a kind to be queued).
  Transitions may reference a trigger.
    The reference will generate a guard, <trigger variable> = TRUE
    And an action <trigger variable> := FALSE.
  Transitions may own a collection of ‘Raise’ actions that reference an internal trigger.
    This will generate an action <trigger variable> := TRUE.
  Trigger may be designated as external event.
    An trigger event will be generated to create a new trigger ( <trigger variable> := TRUE )
    when it has been consumed ( <trigger variable> = FALSE ) and
    no transitions are enabled. (run to completion)
A partial ‘run-to-completion’ semantics will be introduced by disabling all trigger events while any external or internal transition is enabled.

## Slide 31: External Trigger Event
Old trigger has been consumed
Raise new trigger
No transitions enabled

## Slide 32: Triggered transition
The trigger guard
Raise an internal trigger
Consume the external trigger