## Slide 1: Formal Verification of Run-to-completion Style Statecharts Using Event-B

## Slide 2: OUTLINE
Introduction
  Motivation
  Background
    SCXML
    Event-B
    UML-B Statemachine
  Run-to-Completion
Model Construction
SCXML Model Translation to Event-B
Model Verification
Conclusions

## Slide 3: Introduction

## Slide 4: Motivation
Graphical languages are attractive to engineers (e.g. statecharts generalization of statemachines)
Rodin/Event-B support abstraction and refinement and enable the use of formal proofs in earlier stages of the design
There are many definitions of refinement, we are concerned with a refinement that preserves safety properties from one refinement level to the next
To enable our form of refinement statechart transitions cannot cross state containment boundaries arbitrarily.

## Slide 5: State Chart XML (SCXML)
Modeling language based on Harel statechart
Follow a run-to-completion semantics
  Trigger events may enable transitions
  Trigger events are queued whenever a trigger is raised
  A trigger event is de-queued and consumed by firing all transitions that it enables
  Enabled un-triggered transitions are taken repeatedly until none are enabled, and then the next trigger is de-queued
Internal triggers are raised by transitions within the model
External triggers are raise by the environment (non-deterministically)
Internal triggers have higher priority than external triggers
Notes:   Re “A trigger event is de-queued and consumed by firing all transitions that it enables” – of course they have to be in parrallel regions to all be enabled

## Slide 6: Event-B
Formal method for system design via refinement
Event-B models have two parts:
  Contexts: Contain sets, constants and axioms
  Machines: Variables, events, and invariants
Machines are refined to add more details to the model
  Superposition refinement: including additional variables
  Data refinement: replacing abstract variables with new concrete variables
  New events: Refines implicit abstract event that does nothing “skip”
Notes: Data refinement is not used by our SCXML models

## Slide 7: UML-B
Diagrammatic modeling notation for Event-B
Semantics is not UML nor run-to-completion
Only untriggered transitions
Encoding of State :
  Boolean variables
  Enumerated type
Refinements:
  Superposition refinement: add nested statemachines
  Guard strengthening: new guards concerning auxiliary variable
  New Events: add self transitions

## Slide 8: Run-to-Completion
Semantics is specified by an abstract basis that is extended by the model
The basis consist of an Event-B context and machine
Basis Context
Basis Machine

## Slide 9: Statechart Like Representation of Run-to-completion Semantics
Firing Transitions
FIRING
TRIGGERED
FIRING
UN-TRIGGERED
Bold+Italic: Short Description
Italic: Event-B event name
ALL CAPS: STATE NAMES
Completion
NoUntriggeredTransitions
uc = FALSE & dt =
/ uc := TRUE
De-queue Internal Trigger iQ
dequeueInternalTriggered
uc = TRUE & dt =
/ uc := FALSE & dt {: iQ}
De-queue External Trigger eQ
dequeueExternalTriggered
uc = TRUE & dt = & iQ =
/ uc := FALSE & dt {: eQ}
No Triggered Enable
NoTriggeredTransitionsEnable
uc = FALSE & dt
/ dt :=
Fire Triggered
FutureTriggeredTransitions
uc = FALSE & dt
/ dt := & iQ := iQ raisedTriggers
Fire Untriggered
futureUntriggeredTransitionSet
uc = FALSE & dt =
/ iQ := iQ raisedTriggers
Initialisation
/ uc := FALSE & dt := &
iQ := & eQ :=
READY TO DE-QUEUE
Event guards: P1 & P2 / Event action:
Note: P1, P2 are predicates, is a model variable,
and / separates guards from actions
Basis invariants:
Internal and external queue must be disjoint, (iQ eQ) =
At most there shall be one dequeued trigger, dt dt=
Selects a single element from a set iQ and constructs a singleton from it, dt {: iQ}
Notes: Make animation

## Slide 10: Model Construction

## Slide 11: Different Types of Refinement
SA
SB
SC
SD
Our Refinement Rules:
  Nesting Rule : A statechart can be embedded within a state of another statechart
  Guard Strengthening: Guard conditions on a transition can be strengthened
  Action Strengthening: Transitions can have additional actions
Syriani et al. Refinement Rules:
  Rule 2 basic-to-or state rule:
  Rule 3 or-to- and-state rule:
  Rule 7 state extension rule:
  Rule 8 path refinement rule:
SA
SB
SA
SB
SC
SD
SB
SA
SB
SE
SF
SG
SH
SC
SD
SA
SB
SC
SD
x’=0
/x’=x+1
SA
SB
SC
SD
SE
SF
SB
SA
SB
SC
SD
SA
SB
SC
SD
SE
SE
SF
SA
SB
SD
SC

## Slide 12: Quadrotor Helicopter Model Construction
First Abstract Model
  Drone’s basic functionality
  External Triggers: on, toTakeoff, off
  Internal Triggers: toFly, toLand, landed
First Refinement Model
  Apply nesting rule
  Remove some non-determinism by explicitly raising internal trigger toFLy
Notes: Abstraction: Rule 8 path refinement
First Refinement: Rule 2 basic-to-or state rule

## Slide 13: Quadrotor Helicopter Model Construction (cont.)
Second Refinement Model
  Add capability to control flying and battery functionality (nesting rule)
  The charge within the drone battery is monitored by the parallel BATTERYOP state.
  New model variable and guard strengthening
  Internal Triggers: decreaseCharge
Third Refinement Model
  Add implementation details to be able to circumvent flying and proceed to an emergency landing (e.g when battery charge is too low)
  Apply nesting rule
Notes: Second refinement: Rule 4 and-state rule. Introduce a requirement to constrain drone operation to a battery charge of at least 20% capacity.
Third Refinement: Rule 7 state extension rule. data remapping of the abstract states TAKEOFF, CLIMB and HOVER, which should be distinct from the states in this refinement, as the state ABORT is introduced.

## Slide 14: SCXML Model Translation to Event-B

## Slide 15: SCXML Model Translation to Event-B
SCXML models are first translated to UML-B and subsequently to Event-B
  Generation of the basis machine as context that captures generic run-to-completion semantic details
  Generation of events that correspond to all possible combination of each set of transitions that can fire together
  Translation of the SCXML statechart into the corresponding UML-B statemachine
  Translation of the UML-B statemachine into the corresponding Event-B model

## Slide 16: Model Verification

## Slide 17: Verification of Safety Properties Using Theorem Provers
Example Requirement: The control system shall not continue to take off or fly if the battery charge drops below the threshold (say 21%).
  System reacts to low battery charge
  System subsequently leaves the FLY or TAKEOFF states
Ideal Property:
Actual Property:
Ideal Property:
Actual Property:

## Slide 18: Verification of Control Responses Using LTL Model Checking
General form for liveness properties
General liveness property requires the assumption of strong fairness for all events in the model
Example Requirement: The battery charge shall decrease in value after an external trigger event decreaseCharge
The property fails to model check and should be revised as a consequence of the model structure
  The controller only monitors battery charge while in the BATTERYOK state
  Even it the precondition is true the presence of another trigger (e.g off) may take the controller out of the BATTERYOK state
Ideal Property:
Actual Property:

## Slide 19: Conclusions and Future Work

## Slide 20: Conclusions
We have demonstrated a technique for introducing refinement of reactive statecharts that can be translated into Event-B for verification.
Invariant properties about the expected coordination of states can be verified with the Rodin theorem prover. Because of the reactive nature of the system these are interpreted to hold only after the reaction is completed.
We use the LTL model checker to verify expected reactions to environmental triggers. Another kind of liveness property that would be useful to verify is that the ‘run’ converges to completion.
Notes: I.e. transition loops and raised internal triggers do not introduce endless live- lock, but eventually terminate to allow the next external trigger to be consumed.

## Slide 21: Future Work
  Enable the verification of liveness properties using the Roding theorem prover instead of the LTL model checker
  Extend the use of the ‘Scenario Checker’ tool and methods which can animate pre-defined domain specific scenarios at various levels of abstraction. The extension will enable automatic execution of the run to completion.
  Formalize the semantics of the extended SCXML and refinement rules

## Slide 22: QUESTIONS

## Slide 23: Statechart Like Representation of Run-to-completion Semantics
Firing Transitions
FIRING
TRIGGERED
FIRING
UN-TRIGGERED
Bold+Italic: Short Description
Italic: Event-B event name
ALL CAPS: STATE NAMES
Completion
NoUntriggeredTransitions
uc = FALSE & dt =
/ uc := TRUE
De-queue Internal Trigger iQ
dequeueInternalTriggered
uc = TRUE & dt =
/ uc := FALSE & dt {: iQ}
De-queue External Trigger eQ
dequeueExternalTriggered
uc = TRUE & dt = & iQ =
/ uc := FALSE & dt {: eQ}
No Triggered Enable
NoTriggeredTransitionsEnable
uc = FALSE & dt
/ dt :=
Fire Triggered
FutureTriggeredTransitions
uc = FALSE & dt
/ dt := & iQ := iQ raisedTriggers
Fire Untriggered
futureUntriggeredTransitionSet
uc = FALSE & dt =
/ iQ := iQ raisedTriggers
Initialisation
/ uc := FALSE & dt := &
iQ := & eQ :=
READY TO DE-QUEUE
Event guards: P1 & P2 / Event action:
Note: P1, P2 are predicates, is a model variable,
and / separates guards from actions
Basis invariants:
Internal and external queue must be disjoint, (iQ eQ) =
At most there shall be one dequeued trigger, dt dt=
Selects a single element from a set iQ and constructs a singleton from it, dt {: iQ}
Notes: Make animation

## Slide 24: Different Types of Refinement
SA
SB
SC
SD
Our Refinement Rules:
  Nesting Rule : A statechart can be embedded within a state of another statechart
  Guard Strengthening: Guard conditions on a transition can be strengthened
  Action Strengthening: Transitions can have additional actions
Syriani et al. Refinement Rules:
  Rule 2 basic-to-or state rule:
  Rule 3 or-to- and-state rule:
  Rule 7 state extension rule:
  Rule 8 path refinement rule:
SA
SB
SA
SB
SC
SD
SB
SA
SB
SE
SF
SG
SH
SC
SD
SA
SB
SC
SD
x’=0
/x’=x+1
SA
SB
SC
SD
SE
SF
SB
SA
SB
SC
SD
SA
SB
SC
SD
SE
SE
SF
SA
SB
SD
SC